|  | PERMIT TO FLY GENERIC MAINTENANCE SCHEDULE 12 MONTH/150 HOUR INSPECTION | FORM LAA/GMS/12/150 |
| --- | --- | --- |
|  |  | Issue 2 April 2022 |
| AIRCRAFT REG |  | JOB NO |  |
| AIRCRAFT TYPE |  | START DATE |  |
| SERIAL NO |  | TADS REF |  | FINISH DATE |  |
| INSPECTION LOCATION |  | AIRFRAME HOURS |  |
|  |  | HOBBS/TACHO HOURS |  |
| ENGINE (LH) |  | SERIAL NO |  | ENG HOURS |  |
| ENGINE (RH) |  | SERIAL NO |  | ENG HOURS |  |
| PROPELLER (LH) |  | SERIAL NO |  | PROP HOURS |  |
| PROPELLER (RH) |  | SERIAL NO |  | PROP HOURS |  |
| MAINTAINER | NAME |  | SIGNATURE |  |
| MAINTAINER | NAME |  | SIGNATURE |  |
| INSPECTOR | NAME |  | SIGNATURE |  | INSP # |
| INSPECTOR | NAME |  | SIGNATURE |  | INSP # |
| Note: This maintenance schedule should be tailored to the particular aircraft by adding or removing tasks |

| Task Area/Description | Maintainer | Inspector |
| --- | --- | --- |
| Airframe Structure |
| Inspect external structure of fuselage, mainplanes, empennage, cowlings, nacelles, control surfaces, flaps and other high lift devices. |  |  |
| Inspect doors and windows, door hinges and door hinge attachment points. |  |  |
| Operational check of doors, hatches and windows latching and locking. |  |  |
| Inspect internal structure of fuselage, floors, bulkheads, tail booms, mainplanes, nacelles, empennage. Control surfaces, flaps and other high lift devices, structural attachment joint assemblies, struts, bracing wires and their attachments. Note: The need for removal of fabric for detailed inspection of attachments must be assessed when accomplishing this task at the annual check. |  |  |
| Inspect internal corrosion protective treatments, drain holes and paths. |  |  |
| Inspect wooden/Composite Construction: Vent holes, glued joints, bonded assemblies, protective treatments and finishes. Note: The need for removal of fabric for detailed inspection of attachments must be assessed when accomplishing this task. |  |  |
| Inspect static discharge wicks. |  |  |
| Check lightning strike bonding. |  |  |

| Landing Gear |
| --- |
| Inspect landing gear assemblies, shock-absorber struts/units for leaks and correct extension, brake system, brake linings, drums/discs, wheels and tyres. |  |  |
| Service tyre pressures, hydraulic brake system fluid level. |  |  |
| Inspect structural members, attachment fittings, pivot points, shock absorbing devices, bungee rubbers, torque links, shimmy dampers, main wheels, nose/tail wheels, bearings, skids, hoses and lines, hydraulic and electric actuators, jacks, struts, wheel fairing. Note: Carry out with weight off the landing gear. |  |  |
| Operational check of main and parking brake systems. |  |  |
| Operational check of normal/emergency retraction and extension, locking devices, doors and operating linkages, indicators, warning devices. |  |  |
| Check hydraulic/pneumatic operating system. |  |  |

| Flying Controls |
| --- |
| Operational check of primary/secondary flight controls and trim systems for full and free movement in the correct sense. Position indicators agree with surface movement. |  |  |
| Inspect hinges, brackets, push-pull rods, bellcranks, control horns, balance weights, cables, pulleys, chains, tubes, guides, fairleads, rollers, tracks, rails, screw jacks/rams, auxiliary gearboxes and other power-operated systems. Note: The need for removal of flying control cables and control system components for detailed inspection must be assessed when accomplishing this task at the annual check. |  |  |
| Check turnbuckles, locking devices in safety. |  |  |
| Inspect flap asymmetric protection mechanisms. |  |  |
| Inspect condition of struts, control tubes and similar hollow members. |  |  |
| Inspect and operational check electric flap actuation system, limit switches, pitch trim motors. |  |  |
| Check control cables for correct tension, control neutrals and travels. Record results below. |  |  |

| Cable Identification | Temp | Tension | Control Positions | Angle/measurement |
| --- | --- | --- | --- | --- |
|  |  | Required | Actual |  | Required | Actual |
|  | Pt | Stbd |
| AILERON |  |  |  | AILERON UP |  |  |  |
|  |  |  |  | AILERON DOWN |  |  |  |
| ELEVATOR/ STABILATOR |  |  |  | ELEVATOR UP |  |  |
|  |  |  |  | ELEVATOR DOWN |  |  |
| ELEVATOR/ STABILATOR TAB |  |  |  | ELEVATOR TAB UP |  |  |
|  |  |  |  | ELEVATOR TAB DOWN |  |  |
| RUDDER |  |  |  | RUDDER PT/STBD |  |  |  |
| FLAPS |  |  |  | FLAPS UP |  |  |  |
|  |  |  |  | FLAPS TAKE OFF |  |  |  |
|  |  |  |  | FLAPS LANDING |  |  |  |
| AIR BRAKE |  |  |  | AIR BRAKE RETRACTED |  |  |  |
|  |  |  |  | AIR BRAKE EXTENDED |  |  |  |

| Liquid, Air & Gas System |
| --- |
| Inspection of hydraulic, pneumatic, vacuum, other fluid systems. |  |  |
| Service fluid levels in reservoirs, accumulator pressures. |  |  |
| Inspect pitot/static system vents, pitot head, drains clear. Pitot head correctly aligned. |  |  |
| Function check pitot/static system, leak check. |  |  |
| Inspect tanks, powerpacks, valves, pipelines, hoses, actuators, filters, venturis. |  |  |

| Equipment and Environmental |
| --- |
| Inspect seats, seat adjustment and locking, belts/harnesses, attachment, locking and release. |  |  |
| Check fire extinguisher for leakage or discharge (if fitted). |  |  |
| Check fire extinguisher contents by pressure/weight (if fitted). |  |  |
| Inspect cabin air system, heater. |  |  |

| Lubrication |
| --- |
| Lubricate aeroplane, including hinges, bearings, bellcranks, pulleys etc. |  |  |

| Powerplant Installation |
| --- |
| Operational check of engine and propeller controls for full and free movement - throttle, mixture, carburettor heat, alternate air, cowl flaps, propeller pitch. |  |  |
| Inspect powerplant installation. |  |  |
| Inspect alternator/generator drive belt tension and condition. |  |  |
| Inspect crankcase, accessory housings, cylinder assemblies, accessory drive belts, accessories, engine shock mounts, mount frames, bulkheads, firewalls and sealing, cooling baffles, cowlings, breathers and vents, items in engine bay for mutual interference. |  |  |
| Check valve operating mechanism. Next due: |  |  |
| Check cylinder compression and leakage. Record results below. Method: |  |  |

| LH Engine | RH Engine |
| --- | --- |
| Eng Cyl | Results | Eng Cyl | Results | Eng Cyl | Results | Eng Cyl | Results |
| No 1 |  | No 4 |  | No 1 |  | No 4 |  |
|  | 80 |  | 80 |  | 80 |  | 80 |
| No 2 |  | No 5 |  | No 2 |  | No 5 |  |
|  | 80 |  | 80 |  | 80 |  | 80 |
| No 3 |  | No 6 |  | No 3 |  | No 6 |  |
|  | 80 |  | 80 |  | 80 |  | 80 |

| Air Induction |
| --- |
| Inspect air filter, intake and induction system, turbocharger impeller. |  |  |
| Inspect and operational check carburettor heat, alternative air bypass doors, control systems. |  |  |
| Inspect flame traps, drains. |  |  |

| Ignition |
| --- |
| Inspect magnetos, ignition systems, harnesses, leads, switches, starting vibrators, contact breakers, cooling system and ventilators. |  |  |
| Check magneto timing. |  |  |
| Check and service spark plugs. |  |  |

| Exhaust |
| --- |
| Inspect exhaust manifold, mufflers. |  |  |
| Inspect cabin heating system. |  |  |
| Inspect turbocharger, control system, pipelines, hoses. |  |  |

| Engine Lubrication |
| --- |
| Engine oil change, oil filter/screens replace/clean. Next due: |  |  |
| Inspect tanks, sumps, coolers, hoses, pipelines, vents. |  |  |
| Lubricate engine controls. |  |  |
| Inspect engine magnetic plugs. |  |  |

| Fuel System |
| --- |
| Check filters for cleanliness and tank vents unobstructed. Drain samples from all drain points and check for presence of water, foreign matter and correct colour. |  |  |
| Inspect tanks, filler caps, selector valves, pumps, pipelines, hoses, carburettor, injector systems, throttle, mixture control, fuel selector control, filler point placard. |  |  |

| Propeller |
| --- |
| Inspect propeller blades, blade clamps, spinner, backplate. |  |  |
| Inspect hub, constant speed unit, governor, accumulators, motors. |  |  |
| Check pitch change mechanism for backlash. |  |  |
| Lubricate propeller iaw manufacturer’s recommendations. |  |  |

| Electrical Systems |
| --- |
| Inspect and service battery, stowage/compartment, vents and drains. Electrolyte. |  |  |
| Inspect components, wiring, terminals, connectors. |  |  |
| Operational check of warning circuits. |  |  |
| Check correct type and rating of fuses and circuit breakers. Correct spare fuses carried. |  |  |
| Check lamps and lighting. |  |  |
| Operational check all ground operable electrical circuits. Exercise manually operated circuit breakers. |  |  |

| Radio |
| --- |
| Inspect aerials, insulators, controllers, instruments, displays, microphones, headsets, jack plugs and sockets. |  |  |
| Inspect placards and markings for legibility. |  |  |
| Operational check of VHF com (may be carried out on check flight). |  |  |
| Inspect cables and terminals, cooling systems, moisture trap areas. |  |  |

| Instrument Systems |
| --- |
| Check compass ‘deviation’ or ‘steer by’ cards. |  |  |
| Check readings consistent with ambient conditions. Stall warning device operation (if fitted). |  |  |
| Inspect/check instruments/displays. Legibility of markings and associated placards, band ranges and limit markings. |  |  |
| Inspect panels, mounts, pipes, hoses, electrical wiring, gyro filters, flux detectors, instrument transmitters, ADAHRS etc. |  |  |
| Functional check of instruments and indicators - satisfactory condition, mounting, marking and operation. Note: This task is applicable to all instruments and indicators that could affect the airworthiness or operating safety of the aircraft. |  |  |

| Auto-Pilot/Flight Director |
| --- |
| Inspect displays, instruments, controllers. |  |  |
| Operational check of manual override, disengagement functions. |  |  |
| Inspect computers, power supplies, servo motors, connections to flying control systems, automatic trim systems, manometric system interconnections. |  |  |
| Operational check auto-pilot/flight director - all modes (may be carried out on check flight). |  |  |

Repetitive Type/Aircraft-Specific Tasks

| Final Checks (to be carried out after all other tasks are completed) |
| --- |
| Post Ground Run |
| Functional check and inspection of powerplant, liquid, air and gas systems for leaks during and following ground run. |  |  |
| Operational check of instruments, systems and services. Radio for electromagnetic interference. |  |  |
| Following ground run, check to ensure all cowlings, access panels and doors are secure, tools etc removed. |  |  |

| Certification |
| --- |
| Check that all workpack and log book entries have been completed and certified. Ensure all applicable ADs and MPDs have been complied with and certified and SBs have been technically assessed and complied with if required. | N/A |  |
| Check aircraft for compliance with TCDS or TADS (as applicable). | N/A |  |
| Check mandatory placards are installed and legible. | N/A |  |
| Check and review schedule to ensure maintenance needs of the aircraft are being met to assure continuing safe operation. Note: Take account of previous maintenance history, operating environment and utilisation. | N/A |  |
| Issue Permit Maintenance Release | N/A |  |
| PERMIT MAINTENANCE RELEASE |
| The work recorded above has been completed to my satisfaction and in that respect the aircraft is considered fit for flight. |
| Signed | Name | Insp No | Date |

| Engine ground results may be recorded in this table: |  |  |
| --- | --- | --- |
| GROUND RUN RESULTS | NAME |  | NAME |  |
|  | DATE |  | DATE |  |
| OIL PRESSURE |  |  |
| OIL TEMP |  |  |
| CHARGE RATE |  |  |
| MANIFOLD PRESSURE |  |  |
| FUEL FLOW |  |  |
| FUEL PRESSURE |  |  |
| EGT |  |  |
| CHT |  |  |
| POWER CHECK RPM |  |  |
| CARB HEAT/ALTERNATE AIR DROP |  |  |
| SUCTION |  |  |
| LEFT MAG (RPM DROP) |  |  |
| RIGHT MAG (RPM DROP) |  |  |
| PROPELLER CSU CYCLE |  |  |
| MAX RPM |  |  |
| FUEL SELECTOR |  |  |
| FUEL GAUGES |  |  |
| CABIN AIR/HEATER/DEFROST |  |  |
| IDLE RPM |  |  |
| MAG DEAD CUT |  |  |
| BRAKES/STEERING |  |  |
| DI/COMPASS/TC/AH |  |  |
| FLIGHT CONTROLS/TRIMMERS |  |  |
| AUTO PILOT/MANUAL OVER-RIDE |  |  |
| AVIONICS |  |  |